## Slide 1
Design Digitaler Schaltkreise
Synthesis and Timing Analysis Basics
Prof. Ivan Peric ivan.peric@kit.edu
Richard Leys richard.leys@kit.edu
Ilias: https://ilias.studium.kit.edu/goto_produktiv_crs_430424.html

## Slide 2: Lecture Goal
Learn the basics of the Synthesis Steps
Get used to the required data used by synthesis
  Sources, Timing Libraries etc..
Learn the Static Timing Analysis concept:
  Semantic: Timing delay, slew, slack etc…
  Understand setup and hold timing violations
  See how timing reports look like
Learn the basics of timing constraints writing:
  Clock domain
  Input/Output constraining

## Slide 3: Flow overview reminder
HDL
Synthesis
Gates
Place and Route
Final HDL: All logic design + IP are ready, I/Os are set
Add “system” components: PLL, Extra cells like ESD clamps etc…
Design Data: Libraries, Timing Constraints etc..
LEF
LIB
SDC
DEF
.v
.vhd

## Slide 4: Generic Synthesis Flow Reference
Load Libraries
Tool Setup
Load Design
Elaborate
Load Timing Constraints
Synthesis
Mapped
Physical
Incr. optimisation
STA
Output
checks,reports
checks,reports
checks,reports
checks,reports
checks,reports
checks,reports
.v
.vhd
LEF
LIB
SDC
.v
Timing reports
DEF

## Slide 5: Timing Library
Seen low level Flip-Flop and Cells in previous lecture
Timing Library specified for one corner:
  Process Information: Voltage Temperature etc…
  Speed Case: Slow, Typical, Fast
Timing Libraries provide characterisation of cells:
  timing “arcs” between input/outputs
    Ex: Q to CK
  Wire loading models
  Power
  Pin Capacitance etc…
Format used in RTL compiler: Synopsis liberty
library (uk65lscllmvbbr_090c125_wc) {
...
nom_process : 1.0 ;
nom_temperature : 125.0 ;
nom_voltage : 0.9 ;
operating_conditions(uk65lscllmvbbr_090c125_wc) {
process : 1.0;
temperature : 125.0;
voltage : 0.9;
tree_type : balanced_tree
}
...
cell(DFQBM1RA) {
area : 7.200000 ;
cell_footprint : DFQB ;
...
pin(QB) {
capacitance : 0.000000 ;
direction : output ;
...
timing() {
related_pin : "CK" ;
timing_type : rising_edge ;
cell_rise(...) {
}
rise_transition(...) {
}
...
}
...
}
...
}

## Slide 6: Timing Arcs: Delay and Slew
SLEW RATE
rise
fall
A
B
DELAY
rise_transition(...) {
}
cell_rise(...) {
}

## Slide 7: LEF (Library Exchange Format) File
LEF files contain physical information for Cells
Technology rules and specs can be defined
  Ex: Number of layers
  Ex: VIA Definition
Cells physical information include:
  Size
  I/O (Pins) size and locations
  Layer obstructions
Full layout is not included
Using GLADE LEF viewer
LAYER VI1
TYPE CUT ;
SPACING 0.1 ;
SPACING 0.11
ADJACENTCUTS 3 WITHIN 0.14 ;
…
END VI1
ME1
ME2
MACRO SDFQBRM1RA
CLASS CORE ;
SIZE 6.0000 BY 1.8000 ;
SYMMETRY X Y ;
SITE CORE ;
PIN CK
DIRECTION INPUT ;
PORT
LAYER ME1 ;
RECT 1.4400 0.4900 1.5500 0.8900 ;
END
END CK
ENDMACRO

## Slide 8: DEF File
Design Exchange Format
Contains Design Data put together:
  Floorplaning info
  Netlist etc…
Used by Synthesis to load floorplaning information
Floorplan: Size and block, io placements
DEF
Synthesis
Physical

## Slide 9: Synthesis Ready HDL: Top Level
Two types of Top Level HDL
  Partition Module: Just I/O which are pins
  Final Top Level: add instances of real I/O Cells
Partition: Just pins
Top: With IO Cells
1 module xxx (
2
3 input a,
4
5 );
6
7 wire a_internal;
8
9 IUMA a_io(.PAD(a),.DI(a_internal));
10
11
12 mymodule mymodule_I (
13
14 .anotherinput(a_internal)
15 );
16
17 endmodule
Io cell
Core/internal
IO

## Slide 10: Top Level HDL: IP Blocks (RAM example)
All special components acting in the logic design must be instantiated
  Use Provided Verilog, Timing and LEF from Provider
Standard example: RAMS
In FPGA, a RAM is an array, mapped by the tool
In ASIC,the RAM is instantiated
Example in UMC65:
1 module SJKA65_512X32X1CM4 (DOA0,DOA1,DOA2,DOA3,DOA4,DOA5,DOA6,DOA7,DOA8,
2 DOA9,DOA10,DOA11,DOA12,DOA13,DOA14,DOA15,
3 DOA16,DOA17,DOA18,DOA19,DOA20,DOA21,DOA22,
4 DOA23,DOA24,DOA25,DOA26,DOA27,DOA28,DOA29,
5 DOA30,DOA31,DOB0,DOB1,DOB2,DOB3,DOB4,
6 DOB5,DOB6,DOB7,DOB8,DOB9,DOB10,DOB11,DOB12,
7 DOB13,DOB14,DOB15,DOB16,DOB17,DOB18,DOB19,
8 DOB20,DOB21,DOB22,DOB23,DOB24,DOB25,DOB26,
9 DOB27,DOB28,DOB29,DOB30,DOB31,A0,A1,
10 A2,A3,A4,A5,A6,A7,A8,B0,B1,B2,B3,B4,B5,B6,B7,B8,
11 DIA0,DIA1,DIA2,DIA3,DIA4,DIA5,DIA6,DIA7,DIA8,
12 DIA9,DIA10,DIA11,DIA12,DIA13,DIA14,DIA15,
13 DIA16,DIA17,DIA18,DIA19,DIA20,DIA21,DIA22,
14 DIA23,DIA24,DIA25,DIA26,DIA27,DIA28,DIA29,
15 DIA30,DIA31,DIB0,DIB1,DIB2,DIB3,DIB4,
16 DIB5,DIB6,DIB7,DIB8,DIB9,DIB10,DIB11,DIB12,
17 DIB13,DIB14,DIB15,DIB16,DIB17,DIB18,DIB19,
18 DIB20,DIB21,DIB22,DIB23,DIB24,DIB25,DIB26,
19 DIB27,DIB28,DIB29,DIB30,DIB31,WEAN,WEBN,CSAN,
20 CSBN,CKA,DVSE,DVS0,DVS1,DVS2,DVS3,
21 CKB);
LEF
.v
DO[31:0]
512 x 32
entries
entry size

## Slide 11: Elaboration
Parses and compiles the design to an internal logic representation
Basically the same as in any other tool:
  Simulation: irun runs “ncelab”
Check the elaborate output for errors and warnings:
  Unsupported syntax
  Connection width mismatches etc..
Example from counter:
value <= value + 1
Tie-high

## Slide 12: Synthesis: Principle
Two kinds of operations:
  Boolean logic (& , ! , ^ …)
  Arithmetic operators (+,- etc…)
Principle:
  Minimize Boolean logic network
  Map logic and arithmetic to gates and tries to match costs functions:
    Area
    Power
    Timing
Main Focus to be chosen:
  Power ? Area ? Timing?
Usually: Meet timing for performance
ADHM1RA
Sum and Carry out

## Slide 13: Synthesis: Clock Gating example
Clock gating is a good example of synthesis optimisation
It can help save power and modifies timing
Concept:
  If a register value changes when an enable signal is asserted, then remove the clock when not changing
MUX
change
val
No clock gating
val
change
Clock Gating

## Slide 14: STA: Overview
Gate Level + Timing Constraints enable timing the design
Synthesis tries to fix timing during incremental optimisation
Important: Synthesis happens during early implementation stage. Its accuracy is not great.
Two kinds of checks are performed:
  Setup: Make sure logic is not too slow (slow corner)
  Hold: Make sure logic is not too fast (fast corner)
Timing Setup for synthesis: Worst case to ensure it will always work
Elaborate
Synthesis
Incr. optimisation
STA
synthesize –to_mapped
synthesize –to_mapped -incr
.v
Gate netlist
write_hdl > netlist.v

## Slide 15: STA: Setup
Launch!
Capture!
Tco
Clock to output
Trc
Interconnect
Tcomb
Logic
Trc
Interconnect
Tgate
&
&
Trc
Tgate
Tcomb
TSetup
Total
Total
+
-
Positive slack
Negative slack
FIX: Make faster

## Slide 16: STA: Hold
Data must remain stable for Thold after clock period: Cannot be too fast
Total
Thold
Total
+
Total
-
Positive slack: Slow enough
Negative slack: Too Fast
FIX: Make Slower

## Slide 17: STA: Timing Parameters
Mostly two types of delays:
  Gate delays: Input to Output, Clock to output
  Interconnect Delay (RC extraction)
RC extraction is called parasitics extraction:
  R for wire resistance
  C for interconnect capacitance
  Cross-Talking can be extracted (can make RC faster)
&
R
C
Cross-talk
&
Tgate
Trc
Tgate

## Slide 18: STA: Physical Synthesis for wire delays
RC Extraction was done in the past using statistical models
  Estimation of wire length was done based on area and fanout
Starting at ~0.18µ, wire delays become too dominant, so wire delay extraction is required during synthesis -> physical synthesis
Synthesis
Physical
DEF
Fast Place and route
Extraction
STA
Incr. optimisation

## Slide 19: STA: Setup Timing Report example
List of Gates, interconnect and associated timing delay
Sum at the end and check against allowed clock period
Tco
Clock to output
Trc
Interconnect
Tcomb
Tgate
Trc
Tgate
TSetup
Trc
Interconnect
Launch!
Capture!
Tco
Trc
Tgate
.
.
.
TSetup
Type:
Empty for Trc, Gate name otherwise
Slack = (capture - uncertainty) - arrival -71ps = (1300 - 150) - 1221
register
register

## Slide 20: STA: Timing report types
Previous Slide: Register to Register
Other general Timing paths: Register to Output, Input to register, Input to Output
register
output
input
register

## Slide 21: Timing Constraints
Specification for the clocks and paths to be timed
Format in RTL Compiler: Standard Design Constraints (SDC)
The timing analysis uses the constraints to perform analysis
Check Tool documentation
SDC
clock
i/o constraint
i/o constraint
Path constraint
create_clock -name clk -period 1.3 [get_port clk] #750Mhz
set_clock_uncertainty 150 -setup clk # Spare time on setup
set_clock_uncertainty 50 -hold clk # Spare time on hold
set_input_delay -clock clk 50 ...
set_output_delay -clock clk 100 ..
set_load -pin_load 0.15 [all_outputs] #15pf load on outputs

## Slide 22: TC: Clock Definition
Specification:
  Name of the clock
  Period/Waveform
  Start point: Typically the top level input (called port)
Uncertainty: Simply Overconstraining to cover unknown wire delay and physical placement information
  Will be reduced the closer the design gets to its final stage, extraction takes over then.
The named created clock is called a Clock Domain
Later in Place and route: A Clock tree will be created
1 module top (
2
3 input wire clk
4 );
5
6 ....
7
8 endmodule
create_clock -name clk -period 1.3 [get_port clk]
set_clock_uncertainty 150 -setup clk set_clock_uncertainty 50 -hold clk
clk port
Name is arbitrary
In ns per default
Just remove time from period

## Slide 23: Multi-Mode Multi Corner
The may be different constraints, like clock period depending on the mode of operation:
  Test Mode: Clock fed trough a different “slow” input, main clock not active
  Run Mode: Only main clock active
One cannot create two clock domains driving the same logic
Create two modes, which are analysed separately
Corners: Temperature and Voltage combinations
Synthesis: Only check modes
Place and route: perform extraction and analysis on all corners and modes
nT x nV x nM = many corners
Limit to the relevants: will my ASIC be in a -40° environment?

## Slide 24: I/O constraints
Input and Output Delay for the outside world
  Input: When does the input arrive after the clock (setup time from unknown)
  Output:
    How Much time is to be spared for the outside
    How much capacitance do we have to drive
Example from counter:
hold
overflow
set_output_delay
set_load -pin_load
set_input_delay

## Slide 25: False Paths: Non timed wires
Some Special Paths can be ignored
  Configuration Lines if asserted during total inactivity (like reset)
  Asynchronous Reset: Reset usually asserted for a long time, so don’t need to be timed
  Wires not relevant to the mode of operation
1 always @(posedge clk or posedge res_n) begin
2 if (rst) begin
3 // reset
4
5 end
6 else begin
7
8 end
9 end
set_false_path -through [get_port res_n]

## Slide 26: Multi Cycle: timing relaxing
  Some paths can take more time, like configuration Lines barely changing, or changing when design is inactive anyway
  They have to be timed anyways to respect setup and hold time
set_multicycle_path time -setup -through net
N cycles

## Slide 27: Multiple Clock domains
Multiple Clocks can be defined in a design, there are then multiple clock domains
Some clocks are derived from each other, like divided clock
  -> Generated Clocks
  Timing is respected between the clock domains
Separated clocks are uncorrelated, thus false paths are set between flip flops of different clock domains
clk
/ 4
clk_div_4
clk1
clk2
create_generated_clock -divide_by 4 \
–name clk_div_4 –from clk
Design should prevent metastability

## Slide 28: Results
Reports: Final timing and other kind of useful information
Gate Level Netlist
  Use to re-simulate the design
  Go to place and route
LEC tools check netlists for equivalence after each transformation:
  After each synthesis step and incremental optimisation
Place and route setup
  Some scripts to start with encounter
  In real designs, not used in the end but still works for us
Reports

## Slide 29
End Slide