## Slide 1
Design Digitaler Schaltkreise
Semicustom Design Flow introduction

## Slide 2: Lecture Goal
Introduce System Level Design
  Basic concept of Hardware Description Development
Introduce Digital Implementation flow
  Rapid overview
  Some other lectures will go more in details:
    Verilog Design
    Synthesis
    Place and Route 1/2
Übung
  Design and Plan
  Comments are welcome

## Slide 3: System level basics

## Slide 4: System Example: Mixed-Signal Sensor
Analog:
- Amplifier
- Comparator
Full Custom Digital Readout:
- Hit or !Hit
Digital Silicon Photo Multiplier – 350nm – May 2016
Sensor Diode
Light

## Slide 5: System Example: Complex System on Chip
GPUs
Cores
CPU
Routing channels
Support Blocks (PLL, test etc..)
I/O Cells
Iphone A6 APU – 28nm (picture from chipworks.com)

## Slide 6: Stakes in Complex Digital Designs
Features Size decreases, now 65nm is easy to access, next “standard” node for mere mortal is around 28nm, maybe 14nm
Consequences:
  More features per ASIC -> System on Chip
  Each feature gets bigger -> Design and Implementation Cost higher
System Implementation stakes:
  Difficult: Register Transfer level design and verification
  Difficult: System Physical Planning and constraining
  Actual implementations: the tools do the job
Costs Location:
  Hardware Designer Time
  Specification / IP Blocks
  Computation time leads to project-parallelizing

## Slide 7: Analog and Digital implementation Flows
System
Digital
Analog
Schematic Circuit
“Hand-Crafted” Layout
Logic Description (code)
Circuit Synthesis
Technology Mapping
Place and Route
Custom Integration
IPBlocks; Cells
Semi Custom
Full Custom
Fix

## Slide 8: ASIC vs FPGA design
We are interested in Digital ASIC target, not FPGA target
RTL-Level (Verilog/VHDL) design is very similar
FPGA
  FPGA is a build system with pre-available resources
  Synthesis maps to those functions
  Place and route creates configuration file for routing
  Design size and speed is limited
ASIC:
  Every component must be provided and placed
  Example: SRAM memories
  Example: PLL
  Design can be big
  But it’s expensive
Key Point: Resources like RAM/PLL
  What can I get at what Price ?
  ASIC: Buy more IP? Develop them?
  FPGA: Buy a bigger device ?

## Slide 9: System Design Phases
Digital System Specification
HDL Design
System Verification
(simulation)
Implementation
Incremental Changes
Constraints
Timing
Physical
Power

## Slide 10: Design Flow Overview

## Slide 11: Simplified Overview
Verilog/VHDL
Standard Cells
Physical Implementation
Synthesis/Map
Place & Route
Tools
generate
write
Abstract: Hardware Description (HDL = Verilog/VHDL) + Tools
Concrete: Technology Valid implementation

## Slide 12: Hardware Description Methodology
HDL - Register Transfer Level (RTL)
  Verilog / VHDL
System Verification and Metrics
  Simple test benches
  Complex Functional Verification
    UVM with SystemVerilog/e-Language
  Assertions
    “Inline” signal dependencies check
  Coverage
    Detect logic usage
Software Supported design
  Abstract tools for easy design
    FSM designers
    Registerfile generator
    HDL generator
    Etc…
  Language: Often Tool Command Kit (TCL)
  Requires good software skills to develop tools
HDL
Verification

## Slide 13: HDL - Functional Verification
res_n
Verification of Logic by Simulation
The design is called a Device Under Test (DUT)
The Simulation is driven by a testbench:
  Change the Inputs
  Monitor the outputs (“eye” control or software comparisons)
  Test if the outputs are matching specification
The testbench is written in Verilog/VHDL as well…
…but it is just like a software (can use threads etc…)
Testbench type examples:
  Simple Verilog File driving a small design (“eye” control)
  Complex Object-Oriented environment with data randomisation like Universal Verification Methodology (UVM)
counter
clk
clear
hold
value
Simple Test Bench
DUT
Test
code
Monitor
Hold
+1 on clock
Failure
Success

## Slide 14: HDL - Coverage
Coverage gather statistics about the values of the signals encountered during simulation.
They are usually carefully designed
Typical usage:
  A multibit value may be too large and not all the bits are required (ex: Defined 8 bits but value is never > 15 -> only 4 bits enough)
  State machine states are represented by a value (ex 1,2,3 etc…). If a state is never matched, it is either not needed, or can indicate the source of a failure
Example for counter value:
Simulation:
0 -> 16 -> Stop
4 bits hit
Simulation:
0 -> 44 -> Stop
5 bits “hit”
Output from Coverage Analysis Tool

## Slide 15: HDL - Assertions
“Inline” requirements for signal specification inside hardware module definition
Executed during simulation
Usually the simulation stops and fails on assertion error
Very convenient for specification enforcement
Example for counter: Clear behaviour
Counter Verilog code
Clear is 1
Next Clock Cycle
Value is 0
Failure
Success

## Slide 16: Synthesis: Standard cell mapping
Start Point: HDL
Synthesis creates the logic circuit from HDL
Circuits is mapped to Standard Cells
  Standard Cells are VLSI implementation of simple logic functions inside a standard sized block
  Designs Kits provide standard cells
  Each Cell is a logic function implementation:
    Example: AND3 -> AND with 3 inputs
  Timing is provided in Cell description
    Example: Slow/Typical/Fast corners
Mapping is optimised:
  Timing
    Example: Use Low threshold cells
  Area
  Power
AND
AND
AND
AND4
Fixed Height
VDD
VSS
AND
AND4
VDD
VSS
VDD
Physical Placement organised in Rows

## Slide 17: More standard cells
OR
AND
Drain
Source
Gate
-
VDD
GND
OUT
IN

## Slide 18: OR Function Working Principle
OR
A
B
Q
NMOS
PMOS
X
1
X
0
1
0
0
1
0
X
0 = PMOS On ; NMOS Off
1 = PMOS Off; NMOS On
Serie
Parallel
Parallel
Serie
A | B | Q
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1

## Slide 19: Synthesis: Static Timing Analysis (STA)
Lowest Level in Register Transfer Level
  Register – Logic - Register
Timing Constraints:
  Clock cycle definition
  Input/Output Delays
STA:
  D->Q time from FlipFlop
  + Logic (gates + interconnect) time
  Must fit in the clock cycle
    Check setup time: Too slow
    Check hold time: Too Fast
Fixes happen along the whole implementation process
Picture: Uni. Heidelberg – LS Rechnerarchitektur

## Slide 20: Synthesis: Static Timing Analysis (STA)
During Circuit mapping, the STA checks the timing paths
Two delay paths:
  Gate Delay: Given by Standard Cell Specification
  Wire Delay: Interconnection
Wire Delay:
  Small feature size makes wire delay predominant
  Need for physical synthesis

## Slide 21: Synthesis: Physical Synthesis
HDL
Map/Optimize
Fast Place and Route
Extraction
Gates Netlist
Physical part
Verilog file with module instances
Modules are Standard Cell instances
.AND(a,b,net1);
.OR(c,net1,net2);

## Slide 22: Place and Route overview
Gates Netlist
Floorplan
Power Struct.
Place
Clock Tree
Route
Physical Constraints for physical synthesis
Block placement
Core area
I/O Ring
Power stripes
Cell rows
Cells from netlist

## Slide 23: Design For test
After Production, sort:
  Working Ics
  Defect Ics
  Defects/Working = Yield
Tests types:
  Optical defect detection
  Flip-Flop test patterns: JTAG
  Self test for some blocks
    SRAM memories have self testing
  System level test function (like a testbench but in real life)
When to test
  Wafer level during manufacturing
    Expensive
  In Lab/Facility using system level tests
How to implement tests
  Test patterns can be added during synthesis
  System Level:
    Embedded test functionality
    System test: Setup a system and see what happens
ICs
Defect marker
Test probes
Wafer level test example

## Slide 24: Wafer Level / Single Chip Test example
Probe Card with an FPGA
Software drives the Input/Output of the ASIC
Data is readout and Measurements saved to qualify the ASIC
Can be done in chain with the help of a camera driven XYZ table
Probe Card Tester for Belle 2
(ASIC in AMS 180um HV process)
Wafer or Single Chips

## Slide 25: Übung

## Slide 26: Content
Goal: Lear to use Industry tools and get used to the design flow
HDL Design
  Very Simple Hardware Design to learn Verilog/VHDL
    One or multiple counter types is enough
    More Complex System: See PSOC Praktikum im WS16
  Simulation using Cadence INSICIV suite
Synthesis
  Synthesis to a Generic 45nm technology
    Learn about technology data, Logic Cell types etc…
  See some synthesis options like Clock Gating , Reset Types, Physical Synthesis…
  Simulation of Synthesised design
Implementation
  Place the Design in a “ready to produce” ASIC
  Prepare Chip Constraints:
    Target Clocks
    I/O Delays
    Floorplan
  Go through physical implementation with timing checks
  Simulation of placed design with timing information

## Slide 27: Tools: Cadence INSICIV and EDI suites
Simulation: “irun” tool from INSICIV Cadence Suite
Programming: TCL Language
Synthesis:
  Cadence RTL Compiler
Place and route
  Cadence First Encounter
  Also called during physical synthesis
Unlike Analog Design tools:
  Write TCL scripts
  TCL contains function calls for various steps:
    read_design
    elaborate
    read_constraints
    synthesize –to_placed
GUI View:
  See the results of scripts run mostly
  Analyse Timing

## Slide 28: Übung organisation
Groups of ~20
2 groups
Every 2 weeks
Begin: 12th May
Where/When: Thursdays 14h00 at IMS (Westhochschule)
Registration on ILIAS
Overlap with ITIV Hardware Design Lab: OK
  HD-Lab is ok as DDS Übung
  Maybe we will run synthesis on HD-Lab content at the end of semester

## Slide 29
End Slide!