## Slide 1
Design Digitaler Schaltkreise
Introduction to Register Transfer Level design with Verilog
Prof. Ivan Peric ivan.peric@kit.edu
Richard Leys richard.leys@kit.edu

## Slide 2: Goal
Introduce Verilog/VHDL
  Simulation/Synthesisable subsets
  Note the basic semantic (HDL, RTL, DUT etc…)
Understand how basic circuit elements map into Verilog
  We will keep it very simple
Introduce Simulation testbench basics
  Keep it simple as well
Note: Not all syntax elements are presented
Note: You are free to use any languages/tools
Analyse an example together
  Recapitulate what has been seen before
  Play around with the real tools
  Do it yourself during first Übung

## Slide 3: Links
SystemVerilog/Verilog Reference
  http://www.eda.org/sv/SystemVerilog_3.1a.pdf
Some Tutorials on ASIC world
  http://asic-world.com
Linux Command Line:
  http://linuxcommand.org
Open Source Toolchain:
  https://www.idyria.com/access/osi/files/builds/adl/

## Slide 4: INTRODUCTION

## Slide 5: Register Transfer Level (RTL)
Hardware Description Language (HDL)
Verilog or VHDL description model circuits through known operators:
  &, + , << ,>>
  Assignments for combinational logic or register
They have some extra features to model complex designs:
  “Modules” for hierarchies
  Specific technology mapping
  Simulation subset etc…
Register
Register
Logic
Transfer over logic
We will use Verilog in this lecture

## Slide 6: Synthesisable subset
Verilog includes more features than just circuit modelling
Ex: Simulation
  Simulator time synchronisation
  System Verilog: Support for object oriented programming
Careful: Correct simulation does not mean the circuit is synthesisable or feasible
Careful: Synthesisable subset can vary depending on the tools:
  Keep the circuit description simple
HDL: Verilog/SystemVerilog
Synthesisable
! Synthesisable
Maps to logic
Simulation
Other
Check target technology(ies) for reusability

## Slide 7: Simulation Basics
Synthesisable code: Device
Simulation: Test the device
  Drive its inputs
  Check the outputs
  This is a testbench
Simulation code runs like a classical program: Standard programming
Consequence: The simulation is a behavioural model of the device
  Respects Input/Outputs
  Only runs in simulator as “code”
  No logic simulation: Faster
Some models can be in the DUT as well:
  Faster simulation
  IP-Blocks whose logic content is not available
Some Simulation checks are embedded in the DUT:
  Coverage
  Assertions
Device Under Test (DUT)
Testbench
Program running in Simulator
Real logic
Models
Checks (assertion, coverage)
embedded
Run by

## Slide 8: HIERARCHY ELEMENTS

## Slide 9: Hierarchy Modeling?
Circuits have to main components:
  Logic Modeling
  Structure
Think about software:
  Instructions: + , / , -
  Structure: Functions, Classes etc…
Simple Analogy: Flat
  Organisation of the rooms: Hierarchy
  Content of the rooms: primitives
In Verilog:
  Modules
In VHDL:
  Entities
KITCHEN
ROOM
WC
LIVING ROOM
FLAT
NORTH
SOUTH
ROOM
WC
KITCHEN
LIVING ROOM
FLAT

## Slide 10: Hierarchy Example for a CPU
CORE0
CORE1
CORE2
CORE3
Cache
CPU
CACHE
CORES
CORE0
CORE1
CORE2
CORE3
TOP LEVEL
Virtual:
Logical Container for the cores and their interconnections
Instances:
CORE defined only once. 0…3 are copies/instances
Inside Core:
Actual Logic + More Instances (like ALU)

## Slide 11: Hierarchy: Module Definition
A Module is a “box” with
  Input and Outputs
  Logic inside
The modules are instantiated where they are needed
1st Design Rule: All outputs are “reg”
  If not, you don’t know how much combinational logic you end up with
module counter (
input clk ,
output [7:0] reg value
);
always …
…
value <= value +1;
….
endmodule
value
clk
Reg output
Not Reg output
?
What will happen when performing timing analysis ?
8bit counter specification

## Slide 12: Hierarchy: Module Instantiation
Select the name of the module to use
Give the instance a local name
Make connections
module counter (
input clk,
output reg [7:0] value
);
…
endmodule
module parent
…
counter myinstance (
.clk( clk ) ,
.value( value )
);
…
endmodule
definition
instance
.PORTNAME ( LOCAL_NAME )
Name in hierarchy:
parent.myinstance
Mind the parenthesis, commas, semicolons and stuff !!
Connection Syntax

## Slide 13: Parameterised Modules
Modules can have variables in their definition
These variables are overridden when instantiating the module
Counter is a good example:
  The count register width can be made variable
  It matters how wide when actually instantiating (i.e using) the counter
module counter #(parameter W = 8) (
input clk ,
output reg [ W -1 : 0 ] value
);
….
endmodule
8 is the default value if not specified when instantiated

## Slide 14: Hierarchy: Parameterised Module Instantiation
Like a TypeDef in C
There are multiple connection syntax, here is just the detailed safe one
module counter #(parameter W = 8) (
input clk,
output reg [ W – 1 :0] value
);
…
endmodule
counter #(
.W( 2 )
) myinstance (
.clk( clk ) ,
.value( value )
);
definition
instance
2 bit counter!
.PORTNAME( LOCAL VARIABLE )
Mind the parenthesis, commas, semicolons and stuff!!

## Slide 15: Hierachy: Multiple Instanciations
Of course, the same syntax can be used repeatedly inside a module definition
module counter_multiple
…
counter c1 (
.clk(clk),
.value(value0)
);
counter c2 (
.clk(clk),
.value(value1)
);
counter_param #(.W(16)) c3 (
.clk(clk),
.value(value2)
);
endmodule
Same 8bit counter 2 times
Counter with parameter, 16bit
COUNTER MULTIPLE
C1
C2
C3
counter
counter
counter_param

## Slide 16: Circuit MODELING

## Slide 17: Value Representation
4-State Values:
  0
  1
  Z
  X
Register and wires
  Use wire for interconnections
Bus Size
  Like C array
  Use Sublices
}
Logic levels
Unknown
High Impedance
reg a;
wire b;
reg [15:0] c;
wire [1:0] subc = c [12:11];
a
c
16
c
16
subc
11
12

## Slide 18: Clock Synchronous Process definition
Use the always construct
  Define signals triggering the block
  Define edge sensitivity per signal
    Posedge
    Negedge
Process on clock defines clock mapping for all the asynchronous assignments in the block
Multiple Triggers per process:
  One for clock
  One for reset
  More than that: Dangerous for implementation
In Simulation: Does not matter
1 always @(posedge clk or posedge rst) begin
2 if (rst) begin
3 // reset
4
5 end
6 else begin
7
8 end
9 end
}
Reset definition
}
Main Logic

## Slide 19: Value assignments in synchronous block
= : Synchronous -> Combinational logic
<= : Asynchronous -> Register
Reg type
Wire type
<=
=
=
<=
Expression (like C)
value (operator value)?
wire b
reg a
expression
reg/wire
constant
+ , - , & , ^, | , …
3’b000
8’hC3
10 (decimal)
{ N { CONSTANT} } : N * CONSTANT
See reference for all options

## Slide 20: Control Structures and syntax elements
If-else
Cases (like switch in C)
assign
  Simple Variable assignment
Loops for multiple modules instanciation
Blocks are delimited by “begin” … “end”
1 reg a ;
2 reg b ;
3 wire c ;
4
5 assign c = a ^ b ;
6
7 if (c == 1)
8 begin
9 ...
10 end
See reference for all options
Annoying syntax requirements

## Slide 21: Reset Mapping
Skip this subject for now…
…but…
…Design Rule: All signals ALWAYS have a reset value
1 always @(posedge clk or posedge rst) begin
2 if (rst) begin
3 // reset
4
5 end
6 else begin
7
8 end
9 end
}
Reset assignments here!!

## Slide 22: SIMULATION BASICS

## Slide 23: Simulation Setup and basic rules
Testbench is a module
It is like a software that checks the design
  Software written in Verilog/SystemVerilog
By convention called: tb_top , or something with “tb” in name
Environment signals:
  Use always without sensitivity list: runs continuously
    -> Clock generator
  Use initial for a sequence executed at the beginning
    -> Reset
First Golden Rule:
  All signals must have a reset value
  Never keep X in the waveforms after reset
    Exception made for models of analog blocks like SRAMS (undefined until first read)

## Slide 24: Simulation: Time primitives
Synchronisation possible on:
  “#” Pure simulator time
  Signals (wait, @ )
Use these features to write your tests
Simulator time usage
  Write Clock generator
  Write initial sequence
  Static delays in Models
Signal Synchronisation usage
  Easily drive inputs and test outputs
  Example: Wait on clock to change inputs
  Example: React on some output signals to call a task check
1 // Wait 200ns and release reset
2 #200ns res_n = 1;
1 // Wait for Reset to be released
2 wait (res_n==1);

## Slide 25: Other features
Tasks, Functions and so on
Events for complex model description
External Software connection
Complex Verification Environments like UVM (Functional Verification)
Look at the SystemVerilog Reference
Not the focus if the lecture

## Slide 26: COUNTER Example

## Slide 27: Counter Example: Work tasks
Write a counter
Write a testbench
Simulate
Write a Physical top module
Synthesise
counter
Testbench
counter
Physical Top
Gates

## Slide 28: Counter Specification
+1 increment at each clock cycle
Inputs:
  Clock, Reset
  Hold
  Clear
Outputs:
  Value
Parameter:
  Value width
Conditions:
  Output is reg
  All 0 at reset
Function:
  Clear sets all to 0 (like reset here)
  Increment if not hold
1 module counter #(parameter SIZE = 8) (
2
3 // System
4 input clk,
5 input res_n,
6
7 // Control
8 input hold,
9 input clear,
10
11 // Output
12 output reg [SIZE-1:0] value
13
14 );
15
16 always @(posedge clk) begin
17
18 // Reset
19 if (!res_n || clear) begin
20
21 value <= {SIZE {1'b0} };
22
23 end
24 // Main
25 else begin
26
27
28 if (!hold) begin
29
30 value <= value +1;
31
32 end
33
34 end
35 end
36
37 endmodule
}

## Slide 29: Testbench Specification
Module called “top”
No Input/Output (highest level)
Instantiate the counter
  Set counter width
Setup:
  Clock generator
  Reset Sequence
Test Example:
  Assert clear
  Wait 2 cycles
  Value Must be 0
  Assert Hold
  Wait 2 cycles
  Value must be 2
  Release Hold
  Wait two cycles
  Value must be 4
  $finish
1 // Wiring
2 //--------------------
3 logic clk;
4 logic res_n;
5
6 logic hold;
7 logic clear;
8
9 logic [SIZE-1:0] value;
10
11
12 // Instance: Device Under Test (dut)
13 //---------------
14 counter #(.SIZE(SIZE)) dut (
15 .clk(clk),
16 .res_n(res_n),
17
18 .hold(hold),
19 .clear(clear),
20
21 .value(value)
22
23 );
1 module tb_top;
2
3 // Parameter
4 localparam SIZE = 8;
Connections to local wiring
}

## Slide 30: Clock and Reset
Reset: Setup like in logic
Clog gen: Clock of 100Mhz
  10ns period time
  Start Simulator with a time unit of 1ns
1 // Reset
2 initial
3 begin
4 clk = 0;
5 res_n = 0;
6
7 // Functional inital values
8 hold = 0;
9 clear = 0;
10
11 // No reset for value, its reset is in the logic
12
13 // Wait and release reset
14 #50ns res_n = 1;
15
16 end
1 // Clock
2 always
3 begin
4 #5ns clk <= ~clk;
5 end
Reset in logic: good 
Running
All set 

## Slide 31: Write a test
Synchronise on clocks to wait and assert control signals
  Use negedge for better readability
Use normal control structures for tests
  Skip this for now
In case of error: use $error
Not very detailed here
Try in the lab work
Use $finish to stop simulation after your tests
1 //
2 clear = 1;
3 @(negedge clk);
4 @(negedge clk);
5
6 clear = 0;
7 @(negedge clk);
8 @(negedge clk);
9
10 hold = 1;
11 @(negedge clk);
12 @(negedge clk);
13
14 hold = 0;
15 @(negedge clk);
16 @(negedge clk);
17
18
19 #100ns $finish();
}

## Slide 32: Very Simple Synthesis
Create a Real Physical Design
  Create a “top” file, with an instance of the counter
  The size of the counter is then fixed
Use Cadence RTL Compiler
Write a TCL script to read the design data
Write Constraints for Clock
Synthesise
Constraints.sdc
Standard Cells : Slow corner
counter_top.v
Counter
SIZE = 16
clk
res_n
…
IO PORTS

## Slide 33: Summary
Verilog as HDL language:
  Synthesisable subset
    Use to describe the logic
  Non Synthesisable subset
    Mainly just standard code running in simulator
Simulation
  How to write a simple testbench
  Took notice of embedded checks like assertion and coverage, maybe we will see this once in the Lab work
Implementation:
  Create a “Physical” Top with final design, IO and so on
  First step is synthesis
Next step: Do it yourself in the Übung.

## Slide 34
End Slide