## Slide 1
Design Digitaler Schaltkreise
Place and route 2
Prof. Ivan Peric ivan.peric@kit.edu
Richard Leys richard.leys@kit.edu

## Slide 2: Lecture Goal
Understand the basics of Timing Configuration
Understand the concept of Clock Synthesis
See last routing and design completion steps

## Slide 3: Where are we?
Floorplaning is done and set
Input Outputs are set
Power structures have been planned
Standard Cells are placed
Remains:
  Distribute the clock
  Route the design
  Respect Design Rules for manufacturing
  Keep timing within acceptable margins
  Output design data for DRC/LVS and production

## Slide 4: Reminder: Setup/Hold
Clock Relation:
  Setup: Time available before the next clock
  Hold: Time “not available” after a clock cycle
Slow / Fast:
  Setup: Issue if we are too slow, not enough available time
  Hold: Issue if we are too fast, not over the “unavailable” time
  Slow (setup) and Fast (hold) Corners required!!!
Implementation Fixes:
  Setup:
    Faster Logic -> Low VT Cells?
    Pipelining: Divide the logic in more clock periods
    Change Clock: Start next previous Flop-Flip later: Useful skew
  Hold:
    Slow the logic: Add delay Buffers
    Change Clock: Start previous Flip-Flop clock later
Post-Implementation Fixes:
  Setup: Slow the clock…
  Hold: Nothing to be done 
Pipeline Stage
Delay: Clock Skew

## Slide 5: Timing Setup: MMMC
Multi-Mode Multi-Corner
Multi-Mode:
  All configurations in which the ASIC can run, ex: Test mode, Functional
Corners: Timing Characterisation of libraries for different conditions:
  Voltages
  Temperature
  Best Case, Worst Case
Views: Modes + Corners
  Slow Corners: Fix Setup
  Fast Corners: Fix Hold
Modes
Corners
Best, Worst etc…
Test, Functional, Power save etc…
*
views

## Slide 6: Timing Setup: Process & On Chip Variation
OnCHip Variation and Process/Temperature Variation
Wafer
ASICS
X% difference: Process Variation
ASIC
X% difference: On-Chip Variation

## Slide 7: Timing Setup: On Chip Variation
For slower technology nodes (<65nm) On-Chip Variation (OCV) become more and more dominant:
  Two adjacent transistors on the die are different.
  The smaller the technology, the more disparate it gets.
OCV also affects RC extraction for routing lines
OCV adds up as an extraction corner
  Worsens the runtimes
Setup challenges: Technology specific, not always easy to have correct values to setup the tool with.
Difficulty for us: very much process-related, we are not process experts
In an industry context: don’t forget about it!

## Slide 8: Timing Fixes during implementation
In Cadence tools, the optDesign command is used to reclaim timing after each phase:
  Before Clock Tree Synthesis
  Before Routing
  After Routing
Timing Fixes are done for Setup and Hold separately
Fixes may alter manufacturing rules (DRC)
DRC may alter timing:
  Always re-optimise the design along the implementation flow
Ignore this right now:
  No Specific pattern:
    See what he tool does and re-call design optimisation with different options to fix alterations
  Runtimes go higher, not a good idea for the lab work as well

## Slide 9: Clock Tree Synthesis (CTS)
Per-Clock domain:
  1 Clock Source
  Many Sinks
Goal: Clock available at all flip-flops at the same time
Clock net is very constraining:
  Toggles a lot: Power consumption
  Can toggle fast: Signal Integrity aggressor
  Long wires: Difficult to drive and balance
clk
root
Sinks

## Slide 10: CTS: Clock Skew
Clock arrives at Launch and Capture ports
Positive and Negative Skew are possible
Launch
Capture
Tlaunch
Tcapture
Skew = Tcapture - Tlaunch
Positive: Leaves time for setup
Negative: Removes time for setup

## Slide 11: CTS: Semantics
Latency is used to describe the time to reach the sinks
Skew is defined in: Local and Global categories
  Local for related flip-flops
  Global for unrelated flip-flops
clk
Latency
Local Skew
Global Skew

## Slide 12: CTS: Achieving Zero-Skew
There are two types of clock routing:
  Clock Tree: The commonly used path
  Clock mesh: A grid for the clock
    Better Skew, but higher resource usage
Main Goal: No skew
  All flip-flops get the clock at the same time
Zero-Skew clock tree algorithms are available and researched
  Not the focus here
At Lower technology nodes:
  On-Chip Variation influence increases (OCV)
  Clock meshes seem to have a better tolerance to OCV
Rule: Understand what the tool can do, and the advantages for the specific technology and chip size
http://www.design-reuse.com/articles/21019/clock-mesh-benefits-analysis.html

## Slide 13: CTS: Useful Skew example
Feature example: The tool can try to use positive/negative skew to improve setup or hold timing
Use with precaution, first try to meet timing with no fancy feature
Launch
Capture
Tlaunch
Tcapture
Inserted delay

## Slide 14: Clock Tree and IO Timing
Clock Tree Latency usually shows up in timing violations for Input / Output Paths
Reminder:
  Input: Reserve time from clock period for signal to come to us
  Output: Reserve time from clock periode for signal to get to others
Clock Tree Depth: Latency
Latency adds time to clock: Good for input; bad for output
clk
out
Output delay constraint
Remaining time
Latency

## Slide 15: CTS: Report example
clk

## Slide 16: Routing: Global Overview
Finish All data paths routing with accurate extraction
  Fill the core area blanks with filler cells (see technology documentation for cell names)
  Perform Global and detail routing
  Extraction optimises RC and signal integrity quality7
  Timing is analysed and routing adapted in consequence
Blanks
No Blanks
FILLERS

## Slide 17: Routing: Antenna Fixing
Antenna is a risk during manufacturing process
  A discharge may occur through routed floating nets to transistor gates
  Charges Gaher on metal during etching
  IC would not be working if it happens
Fixes:
  Antenna Cells are inserted to ensure discharge occurs into substrate
  Router can add « Layer Bridge »
Routing might also leverage antenna fixing, so the router may route based on timing and Antenna constraints
(wikipedia: Antenna Effect)

## Slide 18: Routing: Antenna Fixing
(wikipedia: Antenna Effect)
Antenna FIX
Poly
Bridge Fix
Metal 1
Metal 2
Metal 2 Build after Metal 1
Metal 2 is Short

## Slide 19: Prepare for Manufacturing
Final Steps before manufacturing:
  Verify and fix DRC
  Retime/Refix design
Perform Metal Filling to fix density DRC
  Reverify/Retime/Refix design
Write out a GDS file
Perform Layout versus Schematic
  Refix design
Good to go!

## Slide 20: Metal Filling
Filling: Add Dummy metal in empty areas
Very Important to ensure metal planarity:
  During Metal Polishing, if the metal density is low, the isolation oxide may get polished more than the metal
  The layer would not be planar anymore and risk damaging the next layer deposition and VIA constrution
Adds parasitic capacitance -> timing is rechecked
Not always done in the tool, other tools can be used
Sometimes the Foundry access service provider does metal filling (ex: Multi Project Wafer funs)
Tracks
Fillers

## Slide 21: Metal Filling
Density fillers

## Slide 22
End Slide