## Slide 1: Design digitaler Schaltkreise

## Slide 2: Speicherelemente - Klassifizierung
Phase-change Random Access Memory
Magnetoresistive Random Access Memory
Ferroelectric Random Access Memory
Halbleiterspeicher
Festwertspeicher
irreversibel
reversibel
ROM
PROM
EPROM
EEPROM
Flash
Schreib-Lese Speicher
statisches RAM
dynamisches RAM
FeRAM
MRAM
PRAM
Flüchtig (volatile)
Permanent (non-volatile)
Clr UV
Clr El
P. mit spez. Geräten
P. bei Herstellung
FF
Cap
Dest RO/Refresh

## Slide 3: Struktur
Word 0
Word 1
Word 2
Word
2N-1
Storage
cell
M
bits
M
bits
S
0
S
1
S
2
A
0
A
1
A N-1
K=
log
2
N
Word 0
Word 1
Word 2
Word
2N-1
Storage
cell
S
0
Input-Output
(
M
bits)
Input-Output
(
M
bits)
S2N-1
Read-Lines
Bit-Lines
Address decoder

## Slide 4: Struktur
Bit line
Read line
Word
Aspect ratio (too high and too narrow layout) may be a problem!
Address decoder
Address

## Slide 5: Struktur
Driver
Multiplexer
Address decoder
Address
Address
Aspect ratio is better

## Slide 6: ROM
Programmiert bei Herstellung
ROM
Schottky Dioden

## Slide 7
Programmiert vor Verwendung
PROM
Fuse

## Slide 8
Programmiert vor Verwendung
PROM
Fuse
HV

## Slide 9
Programmiert vor Verwendung
PROM
Fuse
HV

## Slide 10
Programmiert vor Verwendung
PROM
Fuse
HV

## Slide 11
Programmiert vor Verwendung
PROM
Fuse

## Slide 12: SRAM

## Slide 13
Statische Speicherzellen
Wenn wir den Ausgang des zweiten Inverters mit dem Eingang des ersten verbinden, haben wir Vin = Vout.
Der Zustand der Schaltung liegt im Schnittpunkt der Kennlinie Vout = f(Vin) und der Gerade Vout = Vin.
Vin
Vout
Vin
Vout
Vin=Vout
Vout/Vin=0
Vout/Vin=1(VDD)
Vout/Vin~VDD/2

## Slide 14: Program
SRAM

## Slide 15: Program
SRAM
1
0

## Slide 16: Program
SRAM
1
0

## Slide 17: Program
SRAM
NMOS leitet starker als PMOS
1
0
1
0

## Slide 18: Program
SRAM
?
1
0

## Slide 19: Program
SRAM
?
0
0
1

## Slide 20: Program
SRAM
?
0

## Slide 21: Program
SRAM
1
0

## Slide 22: Program
SRAM
Richtig geschrieben
1
0

## Slide 23: Read
SRAM
1
0
Grosse Kapazitäten

## Slide 24: Read
SRAM
1
0
1
0
Anfangszustand

## Slide 25: Read
SRAM
1
0
1
0

## Slide 26: Read
SRAM
1->0
?
1
0

## Slide 27: Read
SRAM
0
?->1
1
0

## Slide 28: Read
SRAM
0
1
1
0


## Slide 29: Read
SRAM
RAM Zelle überschrieben
0
1
1
0


## Slide 30: Read mit Precharge
SRAM
1
0

## Slide 31: Read mit Precharge
SRAM
1
0

## Slide 32: Read mit Precharge
SRAM
1
0->?
1->0

## Slide 33: Read mit Precharge
SRAM
1
0
0

## Slide 34: Read mit Precharge
SRAM
1
0
Sense Amplifier

## Slide 35: Layout
…
InP
InN
Wr
InP
InN
Wr
Wr
VDD
GND
VDD
GND

## Slide 36: Layout
…
InP
InN
Wr
InP
InN
Wr
Wr
VDD
GND
VDD
GND

## Slide 37: Layout
…
InP
InN
Wr
InP
InN
Wr
Wr
VDD
GND
VDD
GND

## Slide 38: Layout
…

## Slide 39: Layout
…

## Slide 40: Layout
…

## Slide 41: Layout
…

## Slide 42: Layout
…

## Slide 43: Layout
…

## Slide 44: Layout
…

## Slide 45: Write
SRAM
https://www.chipworks.com/about-chipworks/overview/blog/review-tsmc-28-nm-process-technology
AMD 215-0821060 28 nm HP 6T-SRAM at Poly - Plan View SEM

## Slide 46: Write
SRAM
https://www.chipworks.com/about-chipworks/overview/blog/review-tsmc-28-nm-process-technology

## Slide 47: Sense amplifier
M
4
M
1
M
5
M
3
M
2
V
DD
bit
bit
SE
Out
y

## Slide 48: DRAM

## Slide 49: Write
DRAM
Rd
Wr

## Slide 50: Write
DRAM
Rd
Wr

## Slide 51: Write
DRAM
Rd
Wr

## Slide 52: Write
DRAM
Rd
Wr

## Slide 53: Store
DRAM
Rd
Wr
Leckstrom ist Problem, Ladung fliesst ab

## Slide 54: Store
DRAM
Rd
Wr

Leckstrom ist Problem, Ladung fliesst ab

## Slide 55: Read
DRAM
Rd
Wr

## Slide 56: Read
DRAM
Rd
Wr

## Slide 57: Read
DRAM
Rd
Wr

## Slide 58: Read
DRAM
Rd
Wr
Ladung bleibt erhalten

## Slide 59: Write
1 transistor DRAM
Wr/Rd

## Slide 60: Write
1 transistor DRAM
Wr/Rd

## Slide 61: Write
1 transistor DRAM
Wr/Rd

## Slide 62: Write
1 transistor DRAM
Wr/Rd

## Slide 63: Read
1 transistor DRAM
Wr/Rd

## Slide 64: Read
1 transistor DRAM
Wr/Rd

## Slide 65: Read
1 transistor DRAM
Wr/Rd

## Slide 66: Refresh
1 transistor DRAM
Wr/Rd

## Slide 67: Refresh
1 transistor DRAM
Wr/Rd
Refresh

## Slide 68: Refresh
1 transistor DRAM
Wr/Rd
Refresh

## Slide 70
DRAM
Embedded DRAM in Nintendo Wii U GPU fabbed by Renesas (45-nm)
http://chipworksrealchips.blogspot.de/2014/02/intels-e-dram-shows-up-in-wild.html

## Slide 71
DRAM
Embedded DRAM in IBM Power 7+ microprocessor (32-nm)

## Slide 72
DRAM
Intel’s 22-nm embedded DRAM stack

## Slide 73: Permanentspeicher (non-volatile)

## Slide 74: Speicherzugriff
Speicherzugriff
Idee

## Slide 75: Speicherzugriff
Speicherzugriff
Idee

## Slide 76: Speicherzugriff
Speicherzugriff
Idee

## Slide 77: Speicherzugriff
Speicherzugriff
Idee
Fehler!

## Slide 78: Speicherzugriff
Speicherzugriff
Dioden

## Slide 79: Speicherzugriff
Speicherzugriff
Dioden

## Slide 80: Speicherzugriff
Speicherzugriff
Dioden

## Slide 81: Speicherzugriff
Speicherzugriff
Dioden

## Slide 82: Speicherzugriff
Speicherzugriff
Schalter

## Slide 83: Speicherzugriff
Speicherzugriff
Schalter

## Slide 84: Speicherzugriff
Speicherzugriff
Transistor (ODER-Schaltung)
Vth ist hoch

## Slide 85: Speicherzugriff
Speicherzugriff
Transistor (ODER-Schaltung)

## Slide 86: Speicherzugriff
Speicherzugriff
Transistor (ODER-Schaltung)

## Slide 87: Speicherzugriff
Speicherzugriff
Transistor (ODER-Schaltung)

## Slide 88: EPROM, EEPROM und FLASH

## Slide 89: …
Durch die gespeicherte Ladung wird die Schwellspannung des Transistors zu höheren Werten verschoben. Das Auslesen erfolgt bei niedrigen Spannungen. Ist Uth verschoben, schaltet der Transistor nicht ein.
Vgs
Ids
++++++++++++++++++++++++++++++++
- - - - - - - - - - - - - - - - - - - - - - - - - - -
V0 = Q0/C0
V0

## Slide 90: Programmierung - FNT
EPROM program, Fowler-Nordheim tunnelling
++++++++++++++++++++++++++++++++
- - - - - - - - - - - - - - - - - - - - - - - - - - -
-
3.25eV
4.7eV
1.1eV
Zu dick
Durch hohe Spannung wird Barriere dünner

## Slide 91: Programmierung - CHE
EPROM program, channel hot carrier injection
- - - - - - - - - - - - - - - - - - - - - - - - - - -
-
Durch hohen Strom haben
Elektronen hohe Kinetische Energie

## Slide 92: Programmierung
EPROM program

## Slide 93: Feldemission
Bei der Feldemission werden durch ein ausreichend starkes elektrisches Feld (mehr als 109 V/m) Elektronen mit einer sehr geringen Energiebreite aus einer (negativ geladenen) Kathode gelöst. Klassisch betrachtet ist es für ein Teilchen mit einer bestimmten mittleren thermischen Energie, die kleiner ist als die Höhe der Austrittsarbeit, unmöglich, das Kathodenmaterial zu verlassen. Quantenmechanisch betrachtet gibt es jedoch eine bestimmte Wahrscheinlichkeit, dass einzelne Elektronen aus dem Festkörper austreten. Diese werden dann durch das hohe äußere Feld abgesaugt. Diesen Effekt nennt man allgemein auch Tunneleffekt. Das Elektron tunnelt also durch den Potentialwall, der durch das äußere elektrische Feld verkippt wurde – diese spezielle Art von Tunneln nennt man auch „Fowler-Nordheim-Tunneln“ (benannt nach Ralph Howard Fowler und Lothar Nordheim).[1]
Kristall
Vakuum
Gate
Potentialbarriere

## Slide 94: Feldemission
Bei der Feldemission werden durch ein ausreichend starkes elektrisches Feld (mehr als 109 V/m) Elektronen mit einer sehr geringen Energiebreite aus einer (negativ geladenen) Kathode gelöst. Klassisch betrachtet ist es für ein Teilchen mit einer bestimmten mittleren thermischen Energie, die kleiner ist als die Höhe der Austrittsarbeit, unmöglich, das Kathodenmaterial zu verlassen. Quantenmechanisch betrachtet gibt es jedoch eine bestimmte Wahrscheinlichkeit, dass einzelne Elektronen aus dem Festkörper austreten. Diese werden dann durch das hohe äußere Feld abgesaugt. Diesen Effekt nennt man allgemein auch Tunneleffekt. Das Elektron tunnelt also durch den Potentialwall, der durch das äußere elektrische Feld verkippt wurde – diese spezielle Art von Tunneln nennt man auch „Fowler-Nordheim-Tunneln“ (benannt nach Ralph Howard Fowler und Lothar Nordheim).[1]
+
Kristall
Vakuum
Gate
Potentialbarriere

## Slide 95: Löschen - UV
EPROM erase
- - - - - - - - - - -
-
~hv
Ionisierung in SiO2

## Slide 96: Löschen - FNT
EEPROM erase, Fowler-Nordheim tunnelling
-

## Slide 97: EEPROM – verschiedene Möglichkeiten

## Slide 98: Variante 1 Erase and program based on tunnel effect

## Slide 99: Erase
EEPROM (erase and program based on tunnel effect)

## Slide 100: Erase
EEPROM (erase and program based on tunnel effect)
HV
HV

## Slide 101: Erase
EEPROM (erase and program based on tunnel effect)
HV
HV

## Slide 102: Erase
EEPROM (erase and program based on tunnel effect)
Not used

## Slide 103: Program
EEPROM (erase and program based on tunnel effect)

## Slide 104: Program
EEPROM (erase and program based on tunnel effect)
0 1
HV

## Slide 105: Program
EEPROM (erase and program based on tunnel effect)
0 1
HV

## Slide 106: Program
EEPROM (erase and program based on tunnel effect)

## Slide 107: Program
EEPROM (erase and program based on tunnel effect)
1 0

## Slide 108: Program
EEPROM (erase and program based on tunnel effect)
1 0

## Slide 109: Program
EEPROM (erase and program based on tunnel effect)

## Slide 110: Variante 2 Erase based on tunnel effect, program based on hot carriers injection

## Slide 111: Erase particular bit
EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 112: Erase particular bit
EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 113: Erase particular bit
EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 114: Erase particular bit
EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 115: Program particular bit
EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 116: Program particular bit
EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 117: Program particular bit
EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 118: Program particular bit
EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 119: Variante 3 1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 120: Erase
1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 121: Erase
1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 122: Erase
1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 123: Erase
1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 124: Program
1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 125: Program
1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 126: Program
1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 127: Program
1 Transistor EEPROM (erase based on tunnel effect, program based on hot carriers injection)

## Slide 128: FLASH Speicher

## Slide 129: Read
Flash (http://de.slideshare.net/ruchiusha/07flash-memory-technology)
Vgs
Ids
V0

## Slide 130: Read
Flash
Vgs
Ids
V0

## Slide 131: Read
Flash
Vgs
Ids
V0
0
1

## Slide 132: Erase
Flash
Vgs
Ids
V0

## Slide 133: Erase
Flash
Vgs
Ids
V0

## Slide 134: Erase
Flash
Vgs
Ids
V0

## Slide 135: Erase
Flash
Vgs
Ids
V0

## Slide 136: Program
Flash
Vgs
Ids
V0

## Slide 137: Program
Flash
Vgs
Ids
V0

## Slide 138: Program
Flash
Vgs
Ids
V0

## Slide 139: Program
Flash
Vgs
Ids
V0

## Slide 140
Flash is a very popular term when it comes to storage media as it is used by portable devices like phones, tablets, and media players. Flash actually is an offspring of EEPROM, which stands for Electrically Erasable Programmable Read-Only Memory. The main difference between EEPROM and Flash is the type of logic gates that they use. While EEPROM uses the faster NOR (a combination of Not and OR), Flash uses the slower NAND (Not and AND) type. The NOR type is a lot faster than the NAND type but there is the matter of affordability as the former is significantly more expensive than the NAND type.
Another advantage of EEPROM over Flash is in how you can access and erase the stored data. EEPROM can access and erase the data byte-wise or a byte at a time. In comparison, Flash can only do so block-wise. In order to simplify the whole thing, individual bytes are grouped into a smaller number of blocks, which can have thousands of bytes in each block. This is a bit problematic when you only want to read or write to a single byte at a time; which is what’s typically needed in executing the code of a program. This is a reason why Flash cannot be used in electronic circuits that require byte-wise access to data. Data in Flash can also be executed, but it needs to be read as a whole and loaded into RAM beforehand.
EEPROM was designed to be read a lot more than it is written. This is in-line with programming for electronic circuits where you write to the chip a number of times while testing the program. Then, it is stored for good, only to be read every time the data is needed. This is not very suitable for storage media where data is routinely written and read.
In typical use, Flash is used mainly to refer to storage media and can range anywhere from a GB to hundreds of GB. In contrast, EEPROM is usually reserved for permanent code storage in electronic chips. Typical values range from kilobytes to a couple of megabytes. Summary:
1.Flash is just one type of EEPROM 2.Flash uses NAND type memory while EEPROM uses NOR type 3.Flash is block-wise erasable while EEPROM is byte-wise erasable 4.Flash is constantly rewritten while other EEPROMs are seldom rewritten 5.Flash is when large amounts are needed while EEPROM is used when only small amounts are needed

## Slide 141
Der Mechanismus, der die Elektronen durch die isolierende Oxidschicht passieren lässt, wird Fowler-Nordheim-Tunneleffekt genannt (nach ihren ersten Erforschern), d. h. bei einem Flashspeicher handelt es sich um die Anwendung eines nur quantenmechanisch deutbaren Effekts. Um die Wahrscheinlichkeit, dass Elektronen zum Floating-Gate tunneln, zu erhöhen, wird oft das Verfahren CHE (engl. channel hot electron) verwendet: Die Elektronen werden durch Anlegen einer Spannung über dem Kanal, also zwischen Drain und Source, beschleunigt und dadurch auf ein höheres Energieniveau (daher engl. hot) gehoben, wodurch sie schon bei geringeren Spannungen (typischerweise 10 V) zwischen Gate und Kanal zum Floating-Gate tunneln.
Ein Flash-Speicher besteht aus einer bestimmten, von der Speichergröße abhängigen Anzahl einzelner Speicherelemente. Die Bytes oder Worte (typisch durchaus bis 64 Bit) können einzeln adressiert werden. Dabei können sie in einigen Architekturen auch einzeln geschrieben werden, wogegen bei anderen nur größere Datenmengen auf einmal programmiert werden können. In der Regel ist die entgegengesetzte Operation, das Löschen, aber nur in größeren Einheiten, sogenannten Sektoren (meistens ein Viertel, Achtel, Sechzehntel usw. der Gesamtspeicherkapazität) möglich.
Flash-Speicher haben eine begrenzte Lebensdauer, die in einer maximalen Anzahl an Löschzyklen angegeben wird (10.000 bis 100.000 Zyklen für NOR-Flash und bis zu zwei Millionen für NAND-Flash). Dies entspricht gleichzeitig der maximalen Anzahl Schreibzyklen, da der Speicher jeweils blockweise gelöscht werden muss, bevor er wieder beschrieben werden kann. Diese Zyklenzahl wird Endurance (Beständigkeit) genannt. Verantwortlich für diese begrenzte Lebensdauer ist das Auftreten von Schäden in der Oxidschicht im Bereich des Floating-Gates, was das Abfließen der Ladung bewirkt.[3]
Eine andere wichtige Kenngröße ist die Zeit der fehlerfreien Datenhaltung, die Retention.
Ein weiterer Nachteil ist, dass der Schreibzugriff bei Flash-Speicher erheblich langsamer erfolgt als der Lesezugriff. Zusätzliche Verzögerungen können dadurch entstehen, dass immer nur ganze Blöcke gelöscht werden können.
Der Flash-Speicher speichert seine Informationen auf dem Floating-Gate. Bei einem Löschzyklus durchtunneln die Elektronen die Oxidschicht. Dafür sind hohe Spannungen erforderlich. Dadurch wird bei jedem Löschvorgang die Oxidschicht, die das Floating-Gate umgibt, ein klein wenig beschädigt (Degeneration). Irgendwann ist die Isolation durch die Oxidschicht nicht mehr gegeben, die Elektronen bleiben nicht mehr auf dem Floating-Gate gefangen, und die auf der Speicherzelle gespeicherte Information geht verloren. Der Defekt einer einzelnen Zelle macht einen Flash-Speicher jedoch noch lange nicht unbrauchbar.

## Slide 142
Als nichtflüchtiges Speichermedium steht der Flash-Speicher in Konkurrenz vor allem zu Festplatten und optischen Speichern wie DVDs und Blu-ray-Discs.
Ein wesentlicher Vorteil liegt in der mechanischen Robustheit von Flash-Speicher. Demgegenüber sind Festplatten sehr stoßempfindlich (Head-Crash). Häufig ist die Lebensdauer der Steckkontakte (USB-Stecker) der limitierende Faktor.

## Slide 143: Ferroelectric RAM

## Slide 144: Ferroelectric RAM
https://en.wikipedia.org/wiki/Ferroelectric_RAM
Struktur wie DRAM aber der Kondensator ist “permanent”
Reading, however, is somewhat different than in DRAM. The transistor forces the cell into a particular state, say "0". If the cell already held a "0", nothing will happen in the output lines. If the cell held a "1", the re-orientation of the atoms in the film will cause a brief pulse of current in the output as they push electrons out of the metal on the "down" side. The presence of this pulse means the cell held a "1". Since this process overwrites the cell, reading FeRAM is a destructive process, and requires the cell to be re-written if it was changed.
V
Q

## Slide 145: Ferroelectric RAM
….
Flash
dynamisches RAM
FeRAM
EEPROM
EPROM
ROM
Permanent
RW

## Slide 146: Ferroelectric RAM
Polarisation -> high current
V
Q
-
+
+
-
V
Q
V
Q
V
Q
V
Q
V
Q
+
-
+
-
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
1V
2V
3V
4V
5V

## Slide 147: Ferroelectric RAM
Maintaining of palarity -> low current
V
Q
V
Q
V
Q
V
Q
V
Q
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
+
+
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
+
+
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
+
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
4V
2V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
+
3V
+
1V
0V
V
Q

## Slide 148: Ferroelectric RAM
Reversal of polarity -> high current
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
0V
V
Q
-
+
+
-
+
-
-
+
+
-
+
-
+
-
-1V
V
Q
-
-
+
+
V
Q
-
+
-
+
+
-
+
-
+
-
-2V
-
-
+
+
-
+
+
-
+
-
-
-
+
+
-
+
+
-
-3V
-
-
+
+
-
+
+
-
+
-
-
-
+
+
-
+
+
-
-
-
+
+
-
+
+
-
+
-
-
-
+
+
-
+
V
Q

## Slide 149: Ferroelectric RAM
Precharge
5V
0V

## Slide 150: Ferroelectric RAM
Precharge
0V
5V
5V
5V
0V

## Slide 151: Ferroelectric RAM
Precharge
0V
5V
5V
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
5V
0V

## Slide 152: Ferroelectric RAM
Write FERAM
0V
0V
5V
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
5V
0V

## Slide 153: Ferroelectric RAM
Write FERAM
0V
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
5V
0V

## Slide 154: Ferroelectric RAM
Write FERAM
5V
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
5V
0V

## Slide 155: Ferroelectric RAM
Write FERAM
5V
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
5V
0V

## Slide 156: Ferroelectric RAM
Write FERAM
5V
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
0V

## Slide 157: Ferroelectric RAM
Write FERAM
5V
0V
5V
-
+
-
+
-
+
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
0V
Polarity reversal

## Slide 158: Ferroelectric RAM
Write FERAM
5V
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
0V
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-
Polarity reversal

## Slide 159: Ferroelectric RAM
Write FERAM
5V
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
0V
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
+
-
+
-
+
-

## Slide 160: Ferroelectric RAM
Power off
0V
0V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
0V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
0V

## Slide 161: Ferroelectric RAM
Power on
0V
0V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
0V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V

## Slide 162: Ferroelectric RAM
Power on
0V
0V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V

## Slide 163: Ferroelectric RAM
Write SRAM
0V
0V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V

## Slide 164: Ferroelectric RAM
Write SRAM
0V
0.5V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
0V
5V
-
+
-
+
-
+
5V
Polarity reversal

## Slide 165: Ferroelectric RAM
Write SRAM
0V
0.5V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
0.5V
-
+
-
+
-
+
5V
Polarity reversal

## Slide 166: Ferroelectric RAM
Write SRAM
0V
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
0V
-
+
-
+
-
+
5V
+
-
+
-
+
-
+
-
+
-
+
-

## Slide 167: Ferroelectric RAM
Write SRAM
0V
0V
5V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
0V
-
+
+
-
+
-
-
+
+
-
+
-
-
+
+
-
+
-
5V
+
-
+
-
+
-
+
-
+
-